## Slide 1
Oak Ridge Combustion Analysis System (ORCAS)
Flow sensors
Eng. Speed
Nominal input values (ORCAS to EONS):
Diesel_SOI_FF
Diesel_fuel_FF
Ammonia_fuel_FF
Fresh_air_FF
EONS in a BOX
Use feedforward engine commands to run simulator and retrain SNNs (EONS?)
Use measured engine state to calculate diesel fuel control through the SNN (Sim Scheduler?)
System states (ORCAS to EONS):
M_fuel_scaled
M_air_scaled
CA50_scaled
Cost function (ORCAS to EONS):
cost_c
CAN comms
Engine
Simulator
(Python)
Will the cost function be used in the sim modifier?
Feedback control (EONS to ORCAS):
Network ID (EONS to ORCAS):
Mass feedback:
Diesel_fuel_EONS
Effective Q_LHV:
Combustion efficiency:
Q_gross, X_res
CA50
SOI feedback:
Diesel_SOI_EONS
x6.72
x2.26

## Slide 2
Observations: ,
Network output:

## Slide 3: CAN frames
ID 1: STATE_1, 8 byte IEEE Float (ORCAS to EONS)
  Bits 0-64: FUEL_MASS_SCALED
ID 2: STATE_2, 8 byte IEEE Float (ORCAS to EONS)
  Bits 0-64: AIR_MASS_SCALED
ID 3: STATE_3, 8 byte IEEE Float (ORCAS to EONS)
  Bits 0-64: CA50_SCALED
ID 4: COST_STAGE, 8 byte IEEE Float (ORCAS to EONS)
  Bits 0-64: COST_C
ID 5: CONTROL, 8 byte IEEE Float (EONS to ORCAS)
  Bits 0-31: DIESEL_SOI_EONS
  Bits 32-64: DIESEL_FUEL_EONS
ID 6: NET_ID, 8 byte Unsigned Integer (EONS to ORCAS)
  Bits 0-31: NET_ID_START
  Bits 32-64: NET_ID_STOP
ID 7: FF_SOI, 8 byte IEEE Float (ORCAS to EONS)
  Bits 0-64: DIESEL_SOI_FF
ID 8: FF_DIESEL, 8 byte IEEE Float (ORCAS to EONS)
  Bits 0-64: DIESEL_FUEL_FF
ID 9: FF_AMMONIA, 8 byte IEEE Float (ORCAS to EONS)
  Bits 0-64: AMMONIA_FUEL_FF
ID 10: FF_AIR, 8 byte IEEE Float (ORCAS to EONS)
  Bits 0-64: FRESH_AIR_FF